## Slide 1: Automated PetCare System
Daniel Ritter and Matthew Burket

## Slide 2: Background Information
Over 65% of U.S. Households have pets
Of those households, there are 85 million pet cats and 75 millions pet dogs
Estimated 70% of households vacation at least once a year.
Vacation durations ranging from 5 to 14 days

## Slide 3: Problem Statement
Kennels are an expensive recurring cost
Current automated care methods are expensive, lack reliability/control, and only have a singular function

## Slide 4: Solution
Connect and control various apparatuses needed to care for your Cat or Dog
Food, Water, Laser toy
Automate feeding and watering of your pet
Allow owner to control, interact with, and remotely check on the status of the system while away from home

## Slide 5: Project Features
Automated feeding from user-defined daily schedule
Automated watering
System calculates and updates the estimated percent remaining in the food and water reservoirs
User defines parameters: text warnings and reservoir warning levels
System hosts a website that streams a live video feed from the Webcam, allows user to pan/tilt the webcam, and turn on or off the laser toy
System also informs user of food/water reservoir percent remaining statuses via the webpage

## Slide 6: Alternate Designs
Website Layout and functionality
Waterflow Rate Analysis

## Slide 7: Original Website
Boring
Lacked Feedback
Not Mobile Friendly

## Slide 8: Website Final Version
Button orientation
Food/Water Reservoir Status Feedback
Updated Background/ Visual Enhancements

## Slide 9: Waterflow Rate Analysis: Original Version
Used to Estimate a Value Between 2 Known Points
Complicated
Inaccurate
y = y0 + (x – x0)*

## Slide 10: Waterflow Rate Analysis: Final Version
Linear
Power
Exponential
Linear
Exponential
Power

## Slide 11: Watering Flowchart

## Slide 12: Feeding Flowchart

## Slide 13: Webpage Flowchart

## Slide 14: Final Design (The Enclosure and 3D Printed Parts)
Water Bowl Sensor Mount
Snap’y Fit Food/Water Bowls

## Slide 15: Final Design (The Enclosure and 3D Printed Parts)
The Auger
Breadboard Mounts
Raspberry Pi Case
Relay Module Mounts

## Slide 16
120 Volt AC
120 VAC to 12 VDC Power Supply
Raspberry Pi 3 Model B
Motor to Dispense Food
Power Wires
Data Wires
Raspberry Pi Power Supply
8-Channel Relay
Solenoid Valve to Dispense Water
Sensor to Detect Water in Bowl
Sensor to Detect Water in Reservoir
Block Diagram
Laser Toy
Arduino
Power Supply
Arduino
Camera Module

## Slide 17: Testing
a

## Slide 18
Gantt Chart

## Slide 19
Task Hours
Labor (Hours on Tasks) |  |  |  | 
Tasks | Hours |  |  | 
 | Matt | Dan |  | Both
Materials Research | 3 | 3 |  | 6
Microcontroller Research | 1.5 | 10 |  | 11.5
Bluetooth/WIFI Research | 2.5 | 1 |  | 3.5
Power Control Research | 2.5 | 5 |  | 7.5
Food/Water Dispense Rate Research |  | 10 |  | 10
Order Components | 6 | 6 |  | 12
App Development Research | 1 | 20 |  | 21
Design Flowcharts & Tables | 2 | 1 |  | 3
Revise Flowcharts & Tables | 5 | 1 |  | 6
Design Enclosure | 3 | 2 |  | 5
Program Microcontroller | 20 | 100 |  | 120
Design Wiring Layout | 2 | 6 |  | 8
Develop and Test Web Application |  | 15 |  | 15
Wire Components to Microcontroller | 3 | 2 |  | 5
Test Components with Microcontroller | 6 | 15 |  | 21
Troubleshoot and Reprogram Microcontroller | 10 | 33 |  | 43
Build Enclosure | 12 |  |  | 12
Test Enclosure | 4 |  |  | 4
Mount Entire System | 5 | 3 |  | 8
Test & Troubleshoot Entire System | 8 | 8 |  | 16
Final Documentation | 10 | 4 |  | 14
Total | 106.5 | 245 |  | 351.5
Total Hours on Tasks: 351.5 Hours

## Slide 20
Cost of Materials
Automated PetCare System Cost |  |  |  |  |  | 
Item | Quantity | Cost Per Item | Cost | Use | Location Purchased | Notes
PVC Tee | 1 | $ 1.86 | $ 1.86 | Food System | The Home Depot | 
PVC 45 Deg Pipe | 1 | $ 1.44 | $ 1.44 | Food System | The Home Depot | 
2 Pc White Funnel | 1 | $ 0.97 | $ 0.97 | Water System | Walmart | 
Canning Funnel | 1 | $ 1.99 | $ 1.99 | Food System | Tractor Supply Company | 
Snapy Fit SS Bowl | 2 | $ 9.99 | $ 19.98 | Food and Water | Tractor Supply Company | 
Yellow Outlet End | 1 | $ 2.79 | $ 2.79 | Power | Fluder Home & Builder Supply | 3 prong plug
Extension Cord Wire | 1 | $ 3.69 | $ 3.69 | Power | Fluder Home & Builder Supply | Power Cord
5lb Feeding Reservoir | 2 | $ 16.99 | $ 33.98 | Food and Water | Tractor Supply Company | 
5/8 in PVC Tubing | 1 | $ 3.43 | $ 3.43 | Water System | Lowe's | 7 foot - .49 a foot
2 pack Hinge | 1 | $ 3.99 | $ 3.99 | Enclosure | Fluder Home & Builder Supply | 
Handles | 2 | $ 2.99 | $ 5.98 | Enclosure | Fluder Home & Builder Supply | 
Water Solenoid Valve | 1 | $ 8.29 | $ 8.29 | Water System | Amazon | 
Power Supply | 1 | $ 14.98 | $ 14.98 | Power | Amazon | 120VAC to 12VDC
2 pc Water Lever Sensor Right Anlge | 1 | $ 6.55 | $ 6.55 | Water System | Amazon | Sensor for Water Reservoir
2 pc SS Water Level Sensor | 1 | $ 7.66 | $ 7.66 | Water System | Amazon | Sensor for Water Bowl
SainSmart 8-Channel Relay Module | 1 | $ 10.49 | $ 10.49 | Relay | Amazon | 
Raspberry Pi 3 Model B | 2 | $ 39.99 | $ 79.98 | Microcontroller | Walmart | 1 For Each Person in Group
Auger | 1 | $ 3.00 | $ 3.00 | Food System | Donated - Cost Estimated | 3D Printed
Raspberry Pi Case/Mount | 1 | $ 3.00 | $ 3.00 | Enclosure | Donated - Cost Estimated | 3D Printed
Relay Module Mounting Stand | 1 | $ 1.00 | $ 1.00 | Enclosure | Donated - Cost Estimated | 3D Printed
Breadboard Mount | 1 | $ 0.50 | $ 0.50 | Enclosure | Donated - Cost Estimated | 3D Printed
Water Bowl Sensor Mount | 1 | $ 1.50 | $ 1.50 | Enclosure | Donated - Cost Estimated | 3D Printed
Pan/Tilt Servo Module | 2 | $ 19.99 | $ 39.98 | Web Controls | Amazon | 1st module was defective
Lasers | 10 | $ 1.00 | $ 10.00 | Web Controls | Ebay | Came in a 10 Pack
WebCamera | 1 | $ 49.99 | $ 49.99 | Video Feed | WalMart | 
USB Powered HUB | 1 | $ 19.99 | $ 19.99 | Microcontroller | Amazon | Needed to Ease the Power Load on Our Microcontroller
Motor | 1 | $ 30.00 | $ 30.00 | Food System | Donated - Cost Estimated Ebay | Rear Window Volvo Motor
Enclosure Wood | 3 | $ 14.48 | $ 43.44 | Enclosure | Donated - Cost Estimated Lowe's | (Common: 1-in x 12-in x 8-ft; Actual: 0.75-in x 11.25-in x 8-ft) Pine Board - Lowe's: $14.48 each
Miscellaneous Items | 1 | $ 30.00 | $ 30.00 | Other |  | Resistors, Wires, Screws, Clamps, LEDs, etc.
Total Cost |  |  | $ 440.45 |  |  | 
Total Cost of Materials: $440.45

## Slide 21
Cost of Project
Total Cost of Project: $33,393.58
Senior Project Cost Analysis |  |  | 
 |  |  | Equations
Labor Hourly Cost | $ 30.00 | /hour | ($60,000/year)*(1 year/50 weeks)*(1 week/40 hours)
Overhead Cost | $ 45.00 | /hour | Labor Hourly Cost*1.50
Total of Salary and Overhead | $ 75.00 | /hour | Labor Hourly Cost + Overhead Cost
20% Profit Margin for the Company Applied to Labor and Overhead Costs | $ 93.75 | /hour | (Total of Salary and Overhead) / (1-0.2)
Total Cost of Labor, Overhead and Anticipated Profit | $ 32,953.13 |  | Time on Tasks*20% Profit Margin for the Company Applied to Labor and Overhead Costs
Cost of Materials | $ 440.45 |  | 
Total Project Cost for Amortized Engineering Costs | $ 33,393.58 |  | 
Total | $ 33,393.58 |  | 

## Slide 22: Conclusion

## Slide 23: Thank You!
Parents
Chad Walters
Clarance “Hooker” Anderson
Chris McCorkel
Professor Chandana Jayasooriya

## Slide 24: Automated PetCare System
Questions?